Laboratory Goals

- Verify that student is able to read GD & T information from drawing Title Block

- Students will individually measure “Tolerance Test Blocks”

- Students will evaluate alternative methods of producing “Tolerance Test Blocks”

- Students are to critique the machine processes used in the CNC Tool Operation sheets for each Block manufactured

- The mechanical drawing for the “Cart Caster Adapter”(CCA) is presented

- Teams are given copies of the CCA AutoCAD drawing

- Teams will systematically use Project Management concepts to iterate design and manufacturability improvements for the CCA

- Post-Lab Assignments

Pre-lab / lab reading

- Use the Project Management Handout provided in Lab 1 to assist in optimizing manufacturability of the Cart Caster Adapter

- Research methods, as well as tips & tricks, for

  - Providing the customer with an improved product

    - Better tolerances

    - Better product for the intended application

      - Lower cost

      - Better functionality

      - More robust

    - …

  - Reducing the cost of manufacturing

    - Reducing setup time

      - Better jigging

    - Reducing machine time

      - More accurately controlling

        - Spindle speeds

        - Feed rates

    - Less tool wear

    - Reducing dimensioning verification time

    - …

  - Provide better staffing allocation (increasing productivity)

Equipment needed

- Computer with network access

  - AutoCAD

  - BobCad/Cam

  - Boxford Software

- Boxford 190VMCxi and Boxford DUET

- All related cutting tools identified in the related CNC Operations Sheets

  - 2 of the 6mm slot drills

  - 2 of the 8mm slot drills

  - The two (2) drill sizes cited in the CCA AutoCAD drawing

  - Cutting fluid for drilling holes in aluminum

- Lubricating Oil for the Ways

- Oil Can

- Safety Glasses for every student and the instructor

- First Aid Supplies

Parts needed

- 16 billets of aluminum 1” x 1” x 3”

## Lab safety concerns

| sharp edges produced on milling Blocks sharp edges produced on milled refuse oil splashed or wiped into the eyes air blowing particles into the eyes projectile from broken tooling | projectile from launched billet projectile from launched milled refuse trip hazards fire from discarded oily rags |
| --- | --- |

## 1.  Measure “Tolerance Example Blocks” and Material History

- The following table lists all of the “Tolerance Example Blocks” that were produced:

| 00: Position | 06: Symmetry | 12: Total Run out |
| --- | --- | --- |
| 01: Straightness | 07: Diameter | 13: Profile of Line |
| 02: Flatness | 08: Circularity | 14: Profile of Surface |
| 03: Parallelism | 09: Concentricity | 15: Max Material Condition |
| 04: Perpendicularity | 10: Cylindricity |  |
| 05: Angularity | 11: Circular Run out |  |

Table 1: Number & Tolerance type of each Block designed and machined

- Set up all the blocks as individual workstations.  The appropriate measuring tool for making the related measurements should be collocated near each of the Tolerance Measurement Blocks.

- Lay a plain lined sheet of notebook paper upside down near each Tolerance Measurement Block.

- Each person will systematically:

  - make the related measurement.

  - Turn the page over and write their measurement followed by their printed name

  - Turn the page over and go to the next work station

- After all measurements have been made by all students, each 3-person team will enter the Tolerance Example Block number, and all the values measured by everyone into a spreadsheet

- After all information is entered, merge all the spreadsheets into one spreadsheet

- Sort the spreadsheet by the Tolerance Example Block number

- Plot the data points for each Block number in a graph

  - What do you notice?

    - Distribution

    - Outliers

    - …

  - What can you say about the likelihood of a most correct value?

## 2.  CNC Manufacturing and Apparent Variability

As you saw in the last exercise, the variability seen is often times a product of human error.  What can be done to limit the error introduced by humans?

- Make a list of all the instruments used for measuring the different types of tolerances.

  - Under each list ways you believe human error can be reduced

- Get together 3-person teams and assign the different Tolerance Blocks to each team.

  - Each team will spend 30 minutes looking for methods of eliminating human error from those related measurements

    - One person in the textbook

    - One person on the internet

    - One person in the Machinery Handbook

  - After 30 minutes get together and list what you found under each Block

    - Develop a procedure for measuring each block so that measurements are consistent

## 4.  Controlling Human Error

Repeat Section 1

Compare the results

- How did the attempt to control human error affect the graphs?

If the parts were to be manufactured using the new measurement procedures:

- Would the part manufactured be closer in tolerance than before?

  - Why or Why Not?

What other variability in manufacturing exits?

## 5.  Post Laboratory Assignments

What would you recommend for improving this laboratory experience?

- Enter your comments at: http://xxx

Meet with Team Members and correlate all data generated so that each Team Member gets maximum benefit

Review the pre-lab requirements for Lab 8

Get on the internet and research manufacturing variability

A good article to start with is at:

http://www.manufacturing.net/article.aspx?id=7542&menuid=278